## Slide 1: Introduction to FPGA Simulation and Debug

## Slide 2: Objective
Understand and select appropriate debugging tools for FPGA designs.
Hands on use of four different FPGA debug tools
  Simulation
    Modelsim
  Actual Hardware
    In-System Sources and Probes
    Signal Tap Logic Analyzer
    System Console Instrumentation

## Slide 3: Simulation with ModelSim

## Slide 4: Why Simulation?
+ Include wide range of analyses
+ Reduce development costs
+ Brings innovative products faster to market
+ Provide results that are impossible to measure on physical prototype.
+ High visibility of all signals in design
- Can take a very long time to run for large designs or excessive stimulus
- Designer has to predict and create stimulus that matches actual behavior

## Slide 5: Testbenches
A test bench or testing workbench is an environment used to verify the correctness or soundness of a design or model.
Design Under Test
(DUT)
TESTBENCH
Stimulus
Output

## Slide 6: Verilog Testbench Constructs
Timescale
Initial Block
Clock
Stimulus
Note: no module I/O
Runs only once (vs always block)
1st number is units, second is timing resolution
Inputs are reg, outputs are wires
Use $stop vs $finish or simulator closes
Best to change stimulus on the inactive edge of the clock – easier to read waveforms

## Slide 7: Mentor ModelSim Overview
ModelSim is a multi-language HDL (Verilog/VHDL) simulation environment. It can be used independently or Intel Quartus can create startup scripts and link designs to ModelSim.
Intel Quartus has a license to distribute Modelsim-Altera with Quartus .
Free Starter Edition: <=10K lines of code, runs slower

## Slide 8: ModelSim
Create Project
Compile Design
Simulate
OK
Done
Performed in Quartus
Fix Design
NO
YES
Startup Script
Note:
Only functional (non-timing) simulation is supported
Back-annotated timing model gate level simulations are not supported
This script will link in all of external IP libraries so you don’t have to

## Slide 9: ModelSim GUI
Launching ModelSim from Quartus Tools Run Simulation Tool  RTL Simulation
Command Transcript Window
Testbench File
Simulation Objects

## Slide 10: Lab Exercise 1: MODELSIM

## Slide 11: IN-System Sources and probes (issp)

## Slide 12: Why ISSP
+ Quickly set signals to constants: pins or internal nodes
+ Easily monitor signals – non-triggered continuous display
+ Works on actual hardware
- Not triggered – might miss activity

## Slide 13: In-System Sources and Probes
ISSP allows an easy way to drive and sample signals in hardware and provides a dynamic debugging environment.
ISSP Editor consists of a probe function and interface to control the instances during run time.
It is operated over JTAG.
Each instance can drive and toggle values up to 512 signals.
Can create up to 128 instances of ISSP using IP Catalog

## Slide 14: What is JTAG - Joint Test Action Group (IEEE 1149)
JTAG = JTAG is an industry standard for verifying designs and testing printed circuit boards after manufacture. JTAG implements standards for on-chip instrumentation in electronic design automation as a complementary tool to digital simulation.
FPGAs use this bus as one of the means to configure the device and interface with internal structures in the device
Standard 4 or 5 wire bus – used in many digital electronic devices for test and device specific configuration

## Slide 15: USB Blaster Bridge Circuit
Development Kit with Integrated USB Blaster
Host PC
USB to JTAG Bridge
FPGA
USB
JTAG
This device is commonly a small MAX series non-volatile device
FTDI

## Slide 16: In-System Sources and Probes Block Diagram
Host PC
Host PC

## Slide 17: Example Uses
Prototype a front panel with virtual buttons for a FPGA Design
Monitor results of changing design constants
Extensive TCL scripting support to create custom automated design control interfaces

## Slide 18: SignalTap
Embedded Logic Analyzer

## Slide 19: Why Signal Tap
+ Easily monitor signals – using simple to elaborate triggering schemes
+ No external equipment required
+ Don’t need to figure out stimulus since its based on actual hardware
Uses up lots of memory resources inside the chip
Can change timing of design
Requires recompile which takes time

## Slide 20: Debug of a Design with an External Logic Analyzer
Pros:
  System-level debug
  Can store large quantities of data
  Flexible trigger condition
Cons
  Signals must be physically accessible on the board by a probe
  FPGA must have available I/O
  If you need a new signal that isn’t accessible, you must make a new board
  Probe equipment can potentially effect signal integrity
    High quality probes prevents this, but tend to be expensive
  Equipment expensive for hobbyist

## Slide 21: Signal Tap Logic Analyzer
SignalTap is a logic analyzer made of available resources inside the FPGA
  Uses available logic elements to implement the Logic Analyzer
  Samples on-chip signals on the rising edge of a specified clock signal
  View captured data through the standard JTAG connection typically used for programming the device

## Slide 22: Debug of a Design with Signal Tap
Pros:
  Tap signals buried deep in the design
  No unassigned I/Os or routing needed
  Comes free with all versions of Quartus, no external test equipment required
  Tap new signals with the same board by reconfiguring, recompiling, and reprogramming (no re-spin!)
Cons
  Requires additional device resources (memory and logic elements) – doesn’t change base function, but changes timing
  Must have an active JTAG connection

## Slide 23: What is Signal Tap ?

## Slide 24: Create a Signal Tap instance in two ways
Use Signal Tap file (.stp) (recommended)
    Creates a file (.stp) separate from design files
    Convenient features and GUI
2. Use IP Catalog and IP Parameter Editor
    Manually instantiate altera_signaltap_ii_logic_analyzer IP core directly into HDL code or Qsys (Platform Designer)
    Ties the ELA to the signals directly in RTL

## Slide 25: Signal Tap Logic Analyzer Window
Instance Manager
Identifies which instance is being edited in the GUI
Enable/Disable instances quickly
Gives status and resource utilization (LEs and memory)

## Slide 26: Signal Tap Logic Analyzer Window
JTAG Chain Configuration
Built in “Programmer”
Scans the JTAG chain and identifies available devices

## Slide 27: Signal Tap Logic Analyzer Window
Nodes List
Use the Node Finder to add signals to be tapped
Automatically groups busses together and create custom groups

## Slide 28: Signal Tap Logic Analyzer Window
Trigger Conditions and Qualifiers
Data Enable: Saves signal data (disable to save memory)
Trigger Enable: Signal is part of the trigger condition (disable to save LEs)

## Slide 29: Signal Tap Logic Analyzer Window
Trigger Conditions
Add up to 10 trigger conditions
Choose how every node is compared

## Slide 30: Signal Tap Logic Analyzer Window
Trigger Conditions
Add up to 10 trigger conditions
Choose how every node is compared
Choose what action triggers a specific node

## Slide 31: Signal Tap Logic Analyzer Window
Signal Configuration
Advanced trigger control
Select the number of trigger conditions
Trigger In/Out options

## Slide 32: Signal Tap Logic Analyzer Window
Data/Setup Window
Setup allows configuration of nodes and trigger conditions (for making edits)
Data shows the acquired signal information (for viewing results)

## Slide 33: Lab Exercise 2: In-SYSTEM SOURCES AND PROBES Lab Exercise 3: SIGNAL TAP